## Slide 1: Parallel and Distributed Computing Lecture # 2
By,
Dr. Ali Akbar Siddique

## Slide 2: Introduction to Hardware Architectures for Parallel Computing
Parallel computing relies on specialized hardware to achieve high performance.
Different architectures are designed to support parallelism at various levels.
This lecture covers:
  Multi-core and many-core architectures
  GPU architectures
  Shared vs. distributed memory models

## Slide 3: Multi-core vs. Many-core Architectures
Multi-core Architectures
A multi-core processor is a single computing component with two or more independent processing units (cores). Each core can execute instructions independently, allowing for parallel execution.
Characteristics:
Typically 2 to 16 cores in modern CPUs.
Each core has its own L1 cache but may share L2/L3 caches.
Designed for general-purpose computing and optimized for single-threaded performance.
Common in desktops, laptops, and servers.
Example:
Intel Core i7-12700K (12 cores, 20 threads)
AMD Ryzen 9 5900X (12 cores, 24 threads)
Use Case:
Running multiple applications (e.g., web browsing, video streaming, gaming).
Multitasking (e.g., running a code compiler while editing a document).

## Slide 4: Task Distribution in Multi-Core Processor

## Slide 6: Cache Memory – L1, L2, and L3
1. What is Cache Memory?
Cache memory is a small-sized, high-speed memory located close to the CPU.
It stores frequently accessed data and instructions to reduce latency and improve processing speed.
Faster than RAM but smaller in size.
2. Levels of Cache (L1, L2, L3)
Modern processors use a multi-level cache hierarchy to balance speed and size.

## Slide 7: Cache Hierarchy
Cache Level | Size (Typical) | Speed (Latency) | Location | Function
L1 (Level 1) | 32KB - 1MB | Fastest (1-4 cycles) | Inside CPU core | Stores most frequently used instructions & data
L2 (Level 2) | 256KB - 8MB | Slower than L1 (5-20 cycles) | Shared per core or per group | Holds data evicted from L1
L3 (Level 3) | 4MB - 64MB | Slowest (20-50 cycles) | Shared across all cores | Reduces access time for RAM

## Slide 8: Cache Levels – L1
L1 Cache (First Level Cache)
Smallest but fastest cache (closest to the CPU).
Stores immediate instructions and frequently accessed data.
Typically divided into:
  L1 Instruction Cache (L1i) – Stores CPU instructions.
  L1 Data Cache (L1d) – Stores frequently used data.
Example:
When a CPU fetches an instruction, it first looks in the L1 cache before going to L2 or RAM.

## Slide 9: Cache Levels – L2
L2 Cache (Second Level Cache)
Larger than L1 but slightly slower.
Stores data that doesn’t fit in L1.
Can be dedicated per core or shared among multiple cores.
Example:
If L1 cache misses a piece of data, it checks L2 before accessing RAM.

## Slide 10: Cache Levels – L3
L3 Cache (Third Level Cache)
Largest and slowest cache level but still much faster than RAM.
Typically shared across all cores in multi-core CPUs.
Reduces bottlenecks when multiple cores request the same data.
Example:
In gaming or video rendering, L3 cache helps multiple cores access frequently used textures or frame data.

## Slide 11: Cache Performance Impact
A well-optimized cache system reduces CPU-RAM interaction, improving processing speed.
More L1 and L2 cache means faster response times for critical operations.
L3 cache helps in multi-threaded performance (e.g., AI training, video editing).

## Slide 12: Real-World Example (CPU Cache Sizes)
Processor | L1 Cache | L2 Cache | L3 Cache
Intel Core i9-13900K | 80KB per core | 2MB per core | 36MB shared
AMD Ryzen 9 7950X | 64KB per core | 1MB per core | 64MB shared
Apple M2 | 192KB per core | 2MB per core | 16MB shared

## Slide 13: Analogy for Better Understanding
L1 Cache → Like a notepad on your desk (very fast, very small).
L2 Cache → Like a bookshelf next to your desk (a bit slower but larger).
L3 Cache → Like a library in your office building (much larger but slower to access).

## Slide 14: Many-core Architecture
A many-core processor contains a large number of cores (typically dozens to hundreds) optimized for highly parallel workloads. These architectures prioritize parallelism over single-threaded performance.
Characteristics:
Designed for massive parallelism.
Typically found in GPUs and specialized accelerators.
Cores may be simpler and lower power compared to multi-core CPUs.
Used in scientific computing, AI, and simulations.
Example:
NVIDIA A100 GPU (6912 CUDA cores, 432 Tensor cores)
AMD Instinct MI250X (13,312 Stream processors)
Use Case:
Training deep learning models using TensorFlow or PyTorch.
High-performance computing (HPC) workloads like weather modeling.
Rendering 3D graphics in video games or animations.

## Slide 15: Key Components in Many Core Architecture
Cores & L2 Cache:
Each core (processing unit) has access to L2 cache, which stores frequently used data to reduce memory access latency.
The cores are organized in groups, likely representing Streaming Multiprocessors (SMs) in a GPU.
TD (Thread Dispatching) Units:
These units help distribute workloads efficiently among the processing cores.
They manage threads and optimize parallel execution.
GDDR Memory Controllers (MC):
These handle data transfers between the GPU and the global memory (GDDR memory).
GDDR (Graphics Double Data Rate) memory is optimized for high bandwidth.
PCIe Client Logic:
Responsible for communication between the GPU and the CPU/system memory via the PCIe (Peripheral Component Interconnect Express) bus.
Interconnects (Arrows & Rings):
The black arrows and circular connections represent data flow and interconnects that enable efficient communication between processing cores, caches, and memory controllers.

## Slide 16: Key Differences
Feature | Multi-core Architecture | Many-core Architecture
Number of Cores | 2 - 16 cores | Dozens to thousands of cores
Optimization | General-purpose computing | Highly parallel tasks
Cache Structure | L1 per core, shared L2/L3 | Smaller caches, often per group of cores
Thread Handling | Efficient for multitasking | Optimized for high-thread parallelism
Use Cases | General computing, gaming, office apps | AI, scientific computing, simulations

## Slide 17: Analogy for Better Understanding
Multi-core CPUs are like a small team of highly skilled workers, each capable of doing a variety of tasks independently but with limited numbers.
Many-core GPUs are like an army of workers, each handling small, repetitive tasks but at an enormous scale, making them perfect for highly parallel tasks.

## Slide 18: Shared Memory Model
Multiple processors access the same memory space.
Key Characteristics:
Fast data sharing between processors.
Requires synchronization to avoid conflicts (e.g., using mutexes and semaphores).
Example:
Multi-threaded programming in a multi-core processor.

## Slide 19: Distributed Memory Model
Each processor has its own local memory and communicates via a network.
Key Characteristics:
No direct memory access between processors.
Requires message passing (e.g., MPI - Message Passing Interface).
Example:
Supercomputers using distributed clusters to solve large-scale problems

## Slide 20: Shared vs. Distributed Memory
Feature | Shared Memory | Distributed Memory
Memory Access | Single memory space shared by processors | Each processor has its own memory
Communication | Direct memory access | Message passing (e.g., MPI)
Scalability | Limited to memory bandwidth | Highly scalable for large computations
Example | Multi-core CPUs | Cluster computing, cloud systems